PARALLEL AND DISTRIBUTED COMPUTING
L – 19,20
DATE: 10.10.19
FACULTY : PROF. GAYATHRI R.
DHRUBANKA DUTTA, 17BCE1019

Seive of Eratosthenes

CODE :

#include <mpi.h>
#include <math.h>
#include <stdio.h>
#include <stdlib.h>
#include "MyMPI.h"

int main(int argc, char** argv)	{
    int count; /* local prime count */
    double elapsed_time; /* parallel execution time */
    int first; /* index of first multiple */
    int global_count; /* global prime count */
    int high_value; /* highest value on this proc */
    int i;
    int id; /* process id number */
    int index; /* index of current prime */
    int low_value; /* lowest value on this proc */
    int n; /* sieving from 2, ..., n */
    int p; /* number of processes */
    int proc0_size; /* size of proc 0's subarray */
    int prime; /* current prime */
    int size; /* elements in marked string */
    int first_value_index;
    int prime_step;
    int prime_doubled;
    int sqrt_n;
    int prime_multiple;
    int num_per_block;
    int block_low_value;
    int block_high_value;
    int first_index_in_block;
    char* marked; /* portion of 2, ..., n */
    char* primes;

    MPI_Init(&argc, &argv);

    /* start the timer */
    MPI_Barrier(MPI_COMM_WORLD);
    elapsed_time = -MPI_Wtime();

    MPI_Comm_rank(MPI_COMM_WORLD, &id);
    MPI_Comm_size(MPI_COMM_WORLD, &p);

    if (argc != 2) {
        if (id == 0) /* parent process */
        printf("Command line: %s <m>\n", argv[0]);
        MPI_Finalize();
        exit(1);
    } /* if (argc != 2) */

    n = atoi(argv[1]);

    /*
     * Figure out this process's share of the array, as well as the
     * integers represented by the first and last array elements
     */
    low_value = BLOCK_FIRST + BLOCK_LOW(id, p, n - 1) * BLOCK_STEP;
    high_value = BLOCK_FIRST + BLOCK_HIGH(id, p, n - 1) * BLOCK_STEP;
    size = BLOCK_SIZE(id, p, n - 1);

    /*
     * bail out if all the primes used for sieving are not all
     * help by process 0
     */
    proc0_size = (n - 1) / p;

    if ((2 + proc0_size) < (int)sqrt((double)n)) {
        if (id == 0) /* parent process */
        printf("Too many processes\n");
        MPI_Finalize();
        exit(1);
    } /* if */

    // compute primes from 2 to sqrt(n);
    sqrt_n = sqrt(n);
    primes = (char*)calloc(sqrt_n + 1, 1);
    for (prime_multiple = 2;
        prime_multiple <= sqrt_n;
        prime_multiple += 2) {
        primes[prime_multiple] = 1;
    } /* for */

    for (prime = 3; prime <= sqrt_n; prime += 2) {
        if (primes[prime] == 1)
        continue;

        for (prime_multiple = prime << 1;
        prime_multiple <= sqrt_n;
        prime_multiple += prime) {
        primes[prime_multiple] = 1;
        }
    } /* for */

    /*
     * allocate this process' share of the array
     */
    marked = (char*)calloc(size * sizeof(char), 1);
    if (marked == NULL) {
        printf("Cannot allocate enough memory\n");
        MPI_Finalize();
        exit(1);
    } /* if */

    num_per_block = 1024 * 1024;
    block_low_value = low_value;
    block_high_value = MIN(high_value,
        low_value + num_per_block * BLOCK_STEP);

    for (first_index_in_block = 0;
        first_index_in_block < size;
        first_index_in_block += num_per_block) {
        for (prime = 3; prime <= sqrt_n; prime++) {
        if (primes[prime] == 1)
        continue;
        if (prime * prime > block_low_value) {
        first = prime * prime;
        }
        else {
        if (!(block_low_value % prime)) {
        first = block_low_value;
        }
        else {
        first = prime - (block_low_value % prime) +
        block_low_value;
        }
        }

        /*
        * optimization - consider only odd multiples
        * of the prime number
        */
        if ((first + prime) & 1) // is odd
        first += prime;

        first_value_index = (first - BLOCK_FIRST) / BLOCK_STEP -
        BLOCK_LOW(id, p, n - 1);
        prime_doubled = prime << 1;
        prime_step = prime_doubled / BLOCK_STEP;
        for (i = first; i <= high_value; i += prime_doubled) {
        marked[first_value_index] = 1;
        first_value_index += prime_step;
        } /* for */
        }

        block_low_value += num_per_block * BLOCK_STEP;
        block_high_value = MIN(high_value,
        block_high_value + num_per_block * BLOCK_STEP);
    } /* for first_index_in_block */

    /*
     * count the number of prime numbers found on this process
     */
    count = 0;
    for (i = 0; i < size; i++)
        if (!marked[i])
        count++;

    MPI_Reduce(&count, &global_count, 1, MPI_INT,
        MPI_SUM, 0, MPI_COMM_WORLD);

    /*
     * stop the timer
     */
    elapsed_time += MPI_Wtime();

    /* print the results */
    if (id == 0) {
        global_count += 1; /* add first prime, 2 */
        printf("%d primes are less than or equal to %d\n",
        global_count, n);
        printf("Total elapsed time: %10.6fs\n",
        elapsed_time);
    } /* if */

    MPI_Finalize();

    return 0;
}

OUTPUT :